## Slide 1: Wireless Infrastructure Components
Notes: Wireless Infrastructure Components & Wireless Operations
  Wireless networks can provide client mobility, the ability to connect from any location and at any time, and the ability to roam while staying connected. A Wireless LAN (WLAN) is a classification of wireless network that is commonly used in homes, offices, and campus environments. Although it uses radio frequencies instead of cables, it is commonly implemented in a switched network environment and its frame format is similar to Ethernet.
  This chapter covers WLAN technology, components, security, planning, implementation, and troubleshooting. The types of network attacks to which wireless networks are particularly susceptible are discussed.

## Slide 2: Wireless Infrastructure Components
1. Introduction
2. Wireless LAN Concepts
3. Ad Hoc vs. Infrastructure
3. Summary
Notes: This is one of the two topics about wireless technology that I am going to present to you. The material covered in these presentation comes from Cisco Academy Program delivered in “Scaling Networks” curriculum.
I hope that after completing the first topic you will have a clear picture of wireless concepts and the wireless infrastructure components that make up wireless networks. In the next topic, I will discuss wireless operations to bring you to a better understanding of how wireless communication works.

## Slide 3: Objectives
Describe wireless technology and standards.
Describe the components of a wireless infrastructure.
Describe wireless topologies.
Notes: Objectives
After the lesson, you will be able to describe:
  wireless technology and standards.
  the components of a wireless infrastructure.
  wireless topologies.

## Slide 4: Wireless Concepts
Notes: Wireless Concepts

## Slide 5: Wireless Infrastructure Components Supporting Mobility
Productivity is no longer restricted to a fixed work location or a defined time period.
People now expect to be connected at any time and place, from the office to the airport or the home.
Users now expect to be able to roam wirelessly.
Roaming enables a wireless device to maintain Internet access without losing a connection.
Notes: Supporting Mobility
Wireless networks can provide client mobility, the ability to connect from any location and at any time, and the ability to roam while staying connected. A Wireless LAN (WLAN) is a classification of wireless network that is commonly used in homes, offices, and campus environments. Although it uses radio frequencies instead of cables, it is commonly implemented in a switched network environment and its frame format is similar to Ethernet.
This chapter covers WLAN technology, components, security, planning, implementation, and troubleshooting. The types of network attacks to which wireless networks are particularly susceptible are discussed.

## Slide 6: Wireless Infrastructure Components Benefits of Wireless
Increased flexibility
Increased productivity
Reduced costs
Ability to grow and adapt to changing requirements
Notes: Benefits of Wireless
Business networks today are evolving to support people who are on the move. People are connected using multiple devices, including computers, laptops, tablets, and smart phones. This is the vision of mobility where people can take their connection to the network along with them on the road.
There are many different infrastructures (wired LAN, service provider networks) that make this type of mobility possible, but in a business environment, the most important is the wireless LAN (WLAN).
Productivity is no longer restricted to a fixed work location or a defined time period. People now expect to be connected at any time and place, from the office to the airport or the home. Traveling employees used to be restricted to pay phones for checking messages and returning a few phone calls between flights. Now employees can check email, voice mail, and the status of projects on smart phones.
Users now expect to be able to roam wirelessly. Roaming enables a wireless device to maintain Internet access without losing connection.
Play the video in the figure for an example of how wireless networks enable mobility.
There are many benefits to supporting wireless networking, both in the business environment and at home. Some of the benefits include increased flexibility, increased productivity, reduced costs, and the ability to grow and adapt to changing requirements.
Figure 1 provides examples of wireless flexibility for the mobile employee.
Most businesses rely on switch-based LANs for day-to-day operation within the office. However, employees are becoming more mobile and want to maintain access to their business LAN resources from locations other than their desks. Workers want to take their wireless devices to meetings, co-worker’s offices, conference rooms, and even customer sites, all while maintaining access to office resources. Wireless networking provides this type of flexibility. Instead of spending a significant amount of time transporting necessary company material or locating wired connections to access network resources, using the wireless network, LAN resources can be easily made available to a varieties of wireless devices.
Although hard to measure, wireless access can result in increased productivity and more relaxed employees. With wireless networking, employees have the flexibility to work when they want, where they want. They can respond to customer inquiries whether at the office, or out to dinner. They can access email and other work-related resources quickly and easily, providing better management, better and faster results for customers, and increased profits.
Wireless networking can also reduce costs. In businesses with a wireless infrastructure already in place, savings are realized any time equipment changes or moves are required, such as when relocating an employee within a building, or reorganizing equipment or a lab, or moving to temporary locations or project sites.
Another important benefit of wireless networking is the ability to adapt to changing needs and technologies. Adding new equipment to the network is fairly seamless with wireless networking. Consider the wireless connectivity of the home. Users can surf the web from their kitchen table, living rooms, or even outdoors. Home users connect new devices, such as smart phones and smart pads, laptops, and smart televisions.
As shown in Figure 2, a wireless home router allows the user to connect to these devices without the additional cost or inconveniences of running cables to different locations in the home.

## Slide 7: Wireless Infrastructure Components Wireless Technologies
Wireless networks can be classified broadly as:
Wireless personal-area network (WPAN) – Operates in the range of a few feet (Bluetooth).
Wireless LAN (WLAN) – Operates in the range of a few hundred feet.
Wireless wide-area network (WWAN) – Operates in the range of miles.
Bluetooth – An IEEE 802.15 WPAN standard; uses a device-pairing process to communicate over distances up to .05 mile (100m).
Wi-Fi (wireless fidelity) – An IEEE 802.11 WLAN standard; provides network access to home and corporate users, to include data, voice and video traffic, to distances up to 0.18 mile (300m).
Notes: Wireless Technologies
Wireless communications are used in a variety of professions.
Although the mix of wireless technologies is continually expanding, the focus of this discussion is on wireless networks that allow users to be mobile. Wireless networks can be classified broadly as:
  Wireless Personal-Area Networks (WPAN) - Operates in the range of a few feet. Bluetooth or Wi-Fi Direct-enabled devices are used in WPANs.
  Wireless LANs (WLANs) - Operates in the range of a few hundred feet such as in a room, home, office, and even campus environment.
  Wireless Wide-Area Networks (WWANs) - Operates in the range of miles such as a metropolitan area, cellular hierarchy, or even on intercity links through microwave relays.
  Bluetooth - Originally an IEEE 802.15 WPAN standard that uses a device-pairing process to communicate over distances up to .05 mile (100m). Newer Bluetooth versions are standardized by the Bluetooth Special Interest Group (https://www.bluetooth.org/).
  Wi-Fi (wireless fidelity) - An IEEE 802.11 WLAN standard commonly deployed to provide network access to home and corporate users, to include data, voice and video traffic, to distances up to 300m (0.18 mile).
  WiMAX (Worldwide Interoperability for Microwave Access) - An IEEE 802.16 WWAN standard that provides wireless broadband access of up to 30 miles (50 km). WiMAX is an alternative to cable and DSL broadband connections. Mobility was added to WiMAX in 2005 and can now be used by service providers to provide cellular broadband.
  Cellular broadband - Consists of various corporate, national, and international organizations using service provider cellular access to provide mobile broadband network connectivity. First available with 2nd generation cell phones in 1991 (2G) with higher speeds becoming available in 2001 and 2006 as part of the third (3G) and fourth (4G) generations of mobile communication technology.
  Satellite broadband - Provides network access to remote sites through the use of a directional satellite dish that is aligned with a specific geostationary Earth orbit (GEO) satellite. It is usually more expensive and requires a clear line of sight.
There are many types of wireless technologies available. However, the focus of this chapter is on 802.11 WLANs.

## Slide 8: Wireless Infrastructure Components Wireless Technologies (cont.)
Worldwide Interoperability for Microwave Access (WiMAX) – An IEEE 802.16 WWAN standard that provides wireless broadband access of up to 30 mi (50 km).
Cellular broadband – Consists of various corporate, national, and international organizations using service provider cellular access to provide mobile broadband network connectivity.
Satellite Broadband – Provides network access to remote sites through the use of a directional satellite dish.
Notes: Wireless Technologies

## Slide 9: Wireless Infrastructure Components Wi-Fi Certification
The Wi-Fi Alliance certifies Wi-Fi and the following product compatibility:
IEEE 802.11a/b/g/n/ac/ad-compatible.
IEEE 802.11i secure using WPA2™ and Extensible Authentication Protocol (EAP)
Wi-Fi Protected Setup (WPS) to simplify device connections.
Wi-Fi Direct to share media between devices
Wi-Fi Passpoint to simplify securely connecting to Wi-Fi hotspot networks
Wi-Fi Miracast to seamlessly display video between devices
Notes: Wi-Fi Certification
Standards ensure interoperability between devices made by different manufacturers. Internationally, the three organizations influencing WLAN standards are:
  ITU-R - Regulates the allocation of the RF spectrum and satellite orbits.
  IEEE - Specifies how RF is modulated to carry information. It maintains the standards for local and metropolitan area networks (MAN) with the IEEE 802 LAN/MAN family of standards. The dominant standards in the IEEE 802 family are 802.3 Ethernet and 802.11 WLAN. Although the IEEE has specified standards for RF modulation devices, it has not specified manufacturing standards; therefore, interpretations of the 802.11 standards by different vendors can cause interoperability problems between their devices.
  Wi-Fi Alliance - The Wi-Fi Alliance® (http://www.wi-fi.org) is a global, non-profit, industry trade association devoted to promoting the growth and acceptance of WLANs. It is an association of vendors whose objective is to improve the interoperability of products that are based on the 802.11 standard by certifying vendors for conformance to industry norms and adherence to standards.
The Wi-Fi Alliance certifies Wi-Fi and the following product compatibility:
  IEEE 802.11a/b/g/n/ac/ad compatible
  IEEE 802.11i secure using WPA2™ and Extensible Authentication Protocol (EAP)
  Wi-Fi Protected Setup (WPS) to simplify device connections
  Wi-Fi Direct to share media between devices
  Wi-Fi Passpoint to simplify securely connecting to Wi-Fi hotspot networks
  Wi-Fi Miracast to seamlessly display video between devices
Note: Other Wi-Fi certifications products are available such as WMM® (Wi-Fi Multimedia™), Tunneled Direct Link Setup (TDLS), and WMM-Power Save.

## Slide 10: Wireless Infrastructure Components Wireless NICs
Wireless deployment requires:
End devices with wireless NICs
Infrastructure device, such as a wireless router or wireless AP
Notes: Wireless NICs

## Slide 11: Wireless Infrastructure Components Wireless Home Router
A home user typically interconnects wireless devices using a small, integrated wireless router.
These serve as:
access point
Ethernet switch
router
Notes: Wireless Home Router
Organizations providing wireless connectivity to their users require a WLAN infrastructure to provide additional connectivity options.
Note: IEEE 802.11 refers to a wireless client as a station (STA). In this chapter, the term wireless client is used to describe any wireless capable device.

## Slide 12: Wireless Infrastructure Components Business Wireless Solutions
Figure 1
Figure 2
Notes: Business Wireless Solutions
The small business network shown in Figure 1 is an 802.3 Ethernet LAN. Each client (i.e., PC1 and PC2) connects to a switch using a network cable. The switch is the point where the clients gain access to the network. Notice that the wireless AP also connects to the switch. In this example, either the Cisco WAP4410N AP or the WAP131 AP could be used to provide wireless network connectivity.
Wireless clients use their wireless NIC to discover nearby APs advertising their SSID. Clients then attempt to associate and authenticate with an AP, as shown in Figure 2. After being authenticated, wireless users have access to network resources.
Note: Wireless needs of a small organization differ from those of a large organization. Large, wireless deployments require additional wireless hardware to simplify the installation and management of the wireless network.

## Slide 13: Wireless Infrastructure Components Wireless Access Points
Notes: Wireless Access Points
  APs can be categorized as either autonomous APs or controller-based APs.
  1. Autonomous APs
  Autonomous APs, sometimes referred to as heavy APs, are standalone devices configured using the Cisco CLI or a GUI. Autonomous APs are useful in situations where only a couple of APs are required in the network. Optionally, multiple APs can be controlled using wireless domain services (WDS) and managed using CiscoWorks Wireless LAN Solution Engine (WLSE).
  Note: A home router is an example of an autonomous AP because the entire AP configuration resides on the device.
  Figure 1 displays an autonomous AP in a small network. If the wireless demands increase, more APs would be required. Each AP would operate independent of other APs and require manual configuration and management.
  2. Controller-Based APs
  Controller-based APs are server-dependent devices that require no initial configuration. Cisco offers two controller-based solutions. Controller-based APs are useful in situations where many APs are required in the network. As more APs are added, each AP is automatically configured and managed by a WLAN controller.
  Figure 2 displays a controller-based AP in a small network. Notice how a WLAN controller is now required to manage the APs. The benefit of the controller is that it can be used to manage many APs.
  Note: Some AP models can operate in either autonomous mode or in controller-based mode.

## Slide 14: Wireless Infrastructure Components Small Wireless Deployment Solutions
Notes: Small Wireless Deployment Solutions
For small wireless deployment requirements, Cisco offers the following wireless autonomous AP solutions:
  Cisco WAP4410N AP - This AP is ideal for small organization requiring two APs and supporting a small group of users.
  Cisco WAP121 and WAP321 APs - These APs are ideal for small organizations that want to simplify their wireless deployment using several APs.
  Cisco AP541N AP - This AP is ideal for small- to mid-sized organizations that want robust and an easily manageable cluster of APs.
  Note: Most enterprise-level APs support PoE.

## Slide 15: Wireless Infrastructure Components Small Wireless Deployment Solutions (cont.)
Each AP is configured and managed individually.
This can become a problem when several APs are required.
Notes: Small Wireless Deployment Solutions
Each WAP4410N AP is configured and managed individually. This can become a problem when several APs are required.

## Slide 16: Wireless Infrastructure Components Small Wireless Deployment Solutions
Support the clustering of APs without the use of a controller.
Multiple APs can be deployed and pushed to a single configuration to all devices within the cluster, managing the wireless network as a single system without worrying about interference between APs, and without configuring each AP as a separate device.
Notes: Small Wireless Deployment Solutions
For this reason, the WAP121, WAP321, and AP541N APs support the clustering of APs without the use of a controller. The cluster provides a single point of administration and enables the administrator to view the deployment of APs as a single wireless network, rather than a series of separate wireless devices. The clustering capability makes it easy to set up, configure, and manage a growing wireless network. Multiple APs can be deployed and push a single configuration to all the devices within the cluster, managing the wireless network as a single system without worrying about interference between APs, and without configuring each AP as a separate device.
Specifically, the WAP121 and WAP321 support Single Point Setup (SPS), which makes AP deployment easier and faster. SPS helps to enable the wireless LAN to scale up to four WAP121 and up to eight WAP321 devices to provide broader coverage and support additional users as business needs change and grow.
The Cisco AP541N AP can cluster up to 10 APs together and can support multiple clusters.
A cluster can be formed between two APs if the following conditions are met:
  Clustering mode is enabled on the APs.
  The APs joining the cluster have the same Cluster Name.
  The APs are connected on the same network segment.
  The APs use the same radio mode (i.e., both radios use 802.11n.).
Access an online AP541N emulator.

## Slide 17: Wireless Infrastructure Components Large Wireless Deployment Solutions
For larger organizations with many APs, Cisco provides controller-based managed solutions, including the Cisco Meraki Cloud Managed Architecture and the Cisco Unified Wireless Network Architecture.
Cisco Meraki cloud architecture is a management solution used to simplify the wireless deployment. Using this architecture, APs are centrally managed from a controller in the cloud.
Notes: Large Wireless Deployment Solutions
  Organizations requiring the clustering of multiple APs require a more robust and scalable solution. For larger organizations with many APs, Cisco provides controller-based managed solutions, including the Cisco Meraki Cloud Managed Architecture and the Cisco Unified Wireless Network Architecture.
  Note: There are other controller-based solutions, such as the controllers using Flex mode. Visit http://www.cisco.com for more information.
Cisco Meraki Cloud Managed Architecture
  The Cisco Meraki cloud architecture is a management solution used to simplify the wireless deployment. Using this architecture, APs are managed centrally from a controller in the cloud. Cloud networking and management provides centralized management, visibility, and control without the cost and complexity of controller appliances or overlay management software.
  This process reduces costs and complexity. The controller pushes management settings, such as firmware updates, security settings, wireless network, and SSIDs settings to the Meraki APs.
  Note: Only management data flows through the Meraki cloud infrastructure. No user traffic passes through Meraki’s datacenters. Therefore, if the Cisco Meraki cannot access the cloud, the network continues to function normally. This means users can still authenticate, firewall rules remain in place, and traffic flows at full line rate. Only management functions, such as reports and configuration tools are interrupted.
  The Cisco Meraki cloud managed architecture requires the following:
Cisco MR Cloud Managed Wireless APs - Various models exist to address a broad range of wireless deployment.
Meraki Cloud Controller (MCC) - The MCC provides centralized management, optimization, and monitoring of a Meraki WLAN system. The MCC is not an appliance that must be purchased and installed to manage wireless APs. Rather, the MCC is a cloud-based service that constantly monitors, optimizes, and reports the behavior of the network.
Web-based Dashboard - Meraki’s web-based Dashboard performs configuration and diagnostics remotely.

## Slide 18: Wireless Infrastructure Components Large Wireless Deployment Solutions (cont.)
Notes: Large Wireless Deployment Solutions, Cont.

## Slide 19: Wireless Infrastructure Components Large Wireless Deployment Solutions (cont.)
Notes: Large Wireless Deployment Solutions, Cont.

## Slide 20: Wireless Infrastructure Components Wireless Antennas
Cisco Aironet APs can use:
Omnidirectional Wi-Fi Antennas – Factory Wi-Fi gear often uses basic dipole antennas, also referred to as “rubber duck” design, similar to those used on walkie-talkie radios. Omnidirectional antennas provide 360-degree coverage.
Directional Wi-Fi Antennas – Directional antennas focus the radio signal in a given direction, which enhances the signal to and from the AP in the direction the antenna is pointing.
Yagi antennas – Type of directional radio antenna that can be used for long-distance Wi-Fi networking.
Notes: Wireless Antennas
  Most business class APs require the use of external antennas to make them fully-functioning units. Cisco has developed antennas specifically designed for use with 802.11 APs while accommodating specific deployment conditions, including physical layout, distance, and aesthetics.
  Cisco Aironet APs can use:
    Omnidirectional Wi-Fi Antennas - Factory Wi-Fi gear often uses basic dipole antennas, also referred to as “rubber duck” design, similar to those used on walkie-talkie radios. Omnidirectional antennas provide 360-degree coverage and are ideal in open office areas, hallways, conference rooms, and outside areas.
    Directional Wi-Fi Antennas - Directional antennas focus the radio signal in a given direction. This enhances the signal to and from the AP in the direction the antenna is pointing, providing stronger signal strength in one direction and less signal strength in all other directions.
    Yagi antennas - Type of directional radio antenna that can be used for long-distance Wi-Fi networking. These antennas are typically used to extend the range of outdoor hotspots in a specific direction, or to reach an outbuilding.
    The figure displays various Cisco indoor and outdoor antennas.
  IEEE 802.11n/ac/ad use MIMO technology to increase available bandwidth. Specifically, MIMO uses multiple antennas to exchange more data than it would be possible to do using a single antenna. Up to four antennas can be used to increase throughput.
  Note: Not all wireless routers are the same. For instance, entry level 802.11n routers support 150 Mb/s bandwidth using one Wi-Fi radio, and one antenna attached to the unit. To support the higher data rates, an 802.11n router requires more radios and antennas to manage more channels of data in parallel. For example, two radios and two antennas on an 802.11n router support up to 300 Mb/s, while 450 and 600 Mb/s require three and four radios and antennas, respectively.

## Slide 21: 802.11 Wireless Topologies 802.11 Wireless Topology Modes
Notes: 802.11 Wireless Topology Modes
Wireless LANs can accommodate various network topologies. The 802.11 standard identifies two main wireless topology modes:
  Ad hoc mode - When two devices connect wirelessly without the aid of an infrastructure device, such as a wireless router or AP. Examples include Bluetooth and Wi-Fi Direct.

## Slide 22: 802.11 Wireless Topologies 802.11 Wireless Topology Modes (cont.)
Notes: 802.11 Wireless Topology Modes
    Infrastructure mode - When wireless clients interconnect via a wireless router or AP, such as in WLANs. APs connect to the network infrastructure using the wired distribution system (DS), such as Ethernet.

## Slide 23: 802.11 Wireless Topologies Ad Hoc Mode
Tethering (personal hotspot) – Variation of the Ad Hoc topology when a smart phone or tablet with cellular data access is enabled to create a personal hotspot.
Notes: Ad Hoc Mode
  An ad hoc wireless network is when two wireless devices communicate in a peer-to-peer (P2P) manner without using APs or wireless routers. For example, a client workstation with wireless capability can be configured to operate in ad hoc mode enabling another device to connect to it. Bluetooth and Wi-Fi Direct are examples of ad hoc mode.
Note: The IEEE 802.11 standard refers to an ad hoc network as an independent basic service set (IBSS).
  The figure displays a summary of ad hoc mode.
  A variation of the ad hoc topology is when a smart phone or tablet with cellular data access is enabled to create a personal hotspot. This feature is sometimes referred to as Tethering. A hotspot is usually a temporary quick solution that enables a smart phone to provide the wireless services of a Wi-Fi router. Other devices can associate and authenticate with the smart phone to use the Internet connection. The Apple iPhone refers to this as the Personal Hotspot feature, while Android devices refer to as either Tethering or Portable Hotspot.

## Slide 24: 802.11 Wireless Topologies Infrastructure Mode
Notes: Infrastructure Mode
  The IEEE 802.11 architecture consists of several components that interact to provide a WLAN that supports clients. It defines two infrastructure mode topology building blocks: a Basic Service Set (BSS) and an Extended Service Set (ESS).
  1. Basic Service Set
  A BSS consists of a single AP interconnecting all associated wireless clients. In Figure 1, two BSSs are displayed. The circles depict the coverage area within which the wireless clients of the BSS may remain in communication. This area is called the Basic Service Area (BSA). If a wireless client moves out of its BSA, it can no longer directly communicate with other wireless clients within the BSA. The BSS is the topology building block while the BSA is the actual coverage area (the terms BSA and BSS are often used interchangeably).
  The Layer 2 MAC address of the AP is used to uniquely identify each BSS, which is called the Basic Service Set Identifier (BSSID). Therefore, the BSSID is the formal name of the BSS and is always associated with only one AP.

## Slide 25: 802.11 Wireless Topologies Infrastructure Mode (cont.)
Notes: Infrastructure Mode
  2. Extended Service Set
  When a single BSS provides insufficient RF coverage, two or more BSSs can be joined through a common distribution system (DS) into an ESS. As shown in Figure 2, an ESS is the union of two or more BSSs interconnected by a wired DS. Wireless clients in one BSA can now communicate with wireless clients in another BSA within the same ESS. Roaming mobile wireless clients may move from one BSA to another (within the same ESS) and seamlessly connect.
  The rectangular area depicts the coverage area within which members of an ESS may communicate. This area is called the Extended Service Area (ESA). An ESA typically involves several BSSs in overlapping and/or separated configurations.
  Each ESS is identified by an SSID and in an ESS each BSS is identified by its BSSID. For security reasons, additional SSIDs can be propagated through the ESS to segregate the level of network access.
  Note: The 802.11 standard refers to ad hoc mode as an IBSS.

## Slide 26: Summary
WLANs are often implemented in homes, offices, and campus environments.
Only the 2.4, GHz, 5.0 GHz, and 60 GHz frequencies are used for 802.11 WLANs.
The Wi-Fi Alliance certifies that vendor products conform to industry standards and norms.
A STA uses a wireless NIC to connect to an infrastructure device such as a wireless router or wireless AP.
STAs connect using an SSID.
APs can be implemented as standalone devices, in small clusters, or in a larger controller-based network.
Notes: Summary
  WLANs are often implemented in homes, offices, and campus environments. Only the 2.4 GHz, 5.0 GHz, and 60 GHz frequencies are used for 802.11 WLANs. The ITU-R regulates the allocation of the RF spectrum, while IEEE provides the 802.11 standards to define how these frequencies are used for the physical and MAC sublayer of wireless networks. The Wi-Fi Alliance certifies that vendor products conform to industry standards and norms.
  A wireless client uses a wireless NIC to connect to an infrastructure device, such as a wireless router or wireless AP. Wireless clients connect using an SSID. APs can be implemented as standalone devices, in small clusters, or in a larger controller-base network.

## Slide 27: Summary
A Cisco Aironet AP can use an onmidirectional antenna, a directional antenna, or a yagi antenna to direct signals.
IEEE 802.11n/ac/ad use MIMO technology to improve throughput and support up to four antennas, simultaneously.
In ad-hoc mode or IBSS, two wireless devices connect to each other in a P2P manner.
In infrastructure mode, APs connect to network infrastructure using the wired DS.
Each AP defines a BSS and is uniquely identified by its BSSID.
Multiple BSSs can be joined into an ESS.
Using a particular SSID in an ESS provides seamless roaming capabilities among the BSSs in the ESS.
Notes: Summary
  A Cisco Aironet AP can use an omnidirectional antenna, a directional antenna, or a Yagi antenna to direct signals. IEEE 802.11n/ac/ad use MIMO technology to improve throughput and support up to four antennas simultaneously.
  In ad hoc mode or IBSS, two wireless devices connect to each other in a P2P manner.
  In infrastructure mode, APs connect to network infrastructure using the wired DS. Each AP defines a BSS and is uniquely identified by its BSSID. Multiple BSSs can be joined into an ESS. Using a particular SSID in an ESS provides seamless roaming capabilities among the BSSs in the ESS. Additional SSIDs can be used to segregate the level of network access defined by which SSID is in use.
  A wireless client first authenticates with an AP, and then associates with that AP. The 802.11i/WPA2 authentication standard should be used. AES is the encryption method that should be used with WPA2.
  When planning a wireless network, non-overlapping channels should be used when deploying multiple APs to cover a particular area. There should be a 10-15 percent overlap between BSAs in an ESS. Cisco APs support PoE to simplify installation.