## Slide 1: Mobility Series Module 4 – Wireless LAN Security
William H. Wolfe II
Cisco Certified Networking Academy Instructor Trainer

## Slide 2: So now you need wireless AND security…

## Slide 3: Agenda
Overview of WLAN Security
Wireless Vulnerabilities and Threats
Threat Mitigation Technologies
Strong Authentication and Encryption
Centralizing WLAN Authentication
Conclusion/Remarks/Resources

## Slide 4: Overview of WLAN Security

## Slide 5: Wired vs. Wireless Privacy

## Slide 6: Authentication
  Proving identity can be done using:
    Something you know
      Password
      Something you do
    Something you have
      Physical object
      Value read from a device you have
    Something you are
      Biometric reading

## Slide 7: Authenticating Devices vs. Users

## Slide 8: Encryption

## Slide 9: Symmetric and Asymmetric Encryption

## Slide 10: Wireless Threats
  Rogue access points:
    Usually default configuration
    Any client on a rogue access point is a rogue client
  Ad hoc networks:
    Open potential weaknesses
    Occupy one of your channels
  Client misassociation - accessing the right SSID on a rogue AP
  Wireless attacks:
    Management frames spoofing
    Active attacks
    Passive attacks

## Slide 11: Wireless IDS

## Slide 12: Wireless IPS

## Slide 13: Management Frame Protection

## Slide 14: Summary
  In wireless networks, authentication determines who accesses the network, and encryption protects data privacy.
  User authentication can be done using something you know, something you have, or something you are. The devices used to access the network can also be authenticated.
  In wireless networks, encryption is used to add privacy.
  Authentication or encryption keys can be common to a cell or unique to each user.
  Controllers can be linked to Cisco IDS to cut Layer 3-to-Layer 7 attackers completely from the Layer 2 wireless connection.
  In Cisco networks, Management Frame Protection can limit the impact of attacks based on management frames.

## Slide 15: Wireless Vulnerabilities and Threats

## Slide 16: Why Are Wireless LANs Prone to Attack?
Open air nature of RF
Propagation Control is difficult
  No physical barriers to intrusion
Standard 802.11 protocol
  Well-documented and understood
  The most common attacks against WLAN networks are targeted at management frames
Unlicensed
  Easy access to inexpensive technology, for deployments and attack
Wireless Access Outside of Physical/Wired Boundaries
Physical Security
Wired Security
Enterprise Network
Notes: 16

## Slide 17: Need for WLAN Security
Open, Pervasive nature of RF
  Can’t control RF Propagation, don’t need physical access to launch attacks anymore
Business impact of stolen data
  Potential legal and financial implications (specially in retail, healthcare and government verticals)
Innate design, per IEEE 802.11, was designed with basic security needs in mind – times have changed
  Known vulnerabilities over time
  WLANs are easy DoS targets: jamming, floods, man-in-the-middle attacks, and dictionary attacks…
  No protection of 802.11 Management and Control frames, most solutions address 802.11 Data frames only
Need to protect and authorize access to network services and resources

## Slide 18: Security Risk Assessment
Sensitive data
  What is classified as Sensitive varies by organization
  Determined at all levels of an organization what data must be protected from both a legal and business viewpoint
  Appropriate data is protected with proper protection.
  Intellectual property, trade secrets, identity information, financial information, health information, and employee and customer databases
  Possibility that some data is too high a security risk
Network services
  Availability of a company's network, and such actions would cause damage to the company's productivity and affect sales.
  Services : E-mail services, file servers, database services, directory services, Internet connectivity, Web-based applications, virus and intrusion detection services, and custom application services.
Notes: 18

## Slide 19: Security Policy and what it means
Security Policy
  An organization needs a security policy to define how to protect sensitive data and network services.
  What to do if systems or policies fail..
Network services
  IT organization needs to work with the Security organization to help define the Security Policy and deploy network services inline with the Security Policy
Client Capabilities
  Understanding the capabilities of the network and more importantly the capabilities of the client endpoints will ensure a secure WLAN deployment able to meet the requirements of the business.
Notes: 19

## Slide 20: Why Is WLAN Security Important?
Hackers/Criminal
Lessons:
Do not rely on basic WEP encryption; requirement for enterprise class security (WPA, EAP/802.1x protocols, Wireless IDS, VLANs/SSIDs, etc.)
Employees often install WLAN equipment on their own (compromises security of your entire network)
Business impact due to stolen data: Potential financial and legal consequences (laws to protect data confidentiality; example: healthcare, retail, financial, government)
“War Driving”
Employees
Vulnerabilities:
Notes: 20
20
Why WLAN Security is important?
  It is all about providing Secure Mobility!
Past History related to WEP, etc
Users installing unauthorized APs
  Out-of-the box configuration of an AP
Government Laws
  Health-Care: Theft of patient care data (ex: HIPPA in US)
  Financial: Theft of financial data
  Government: Theft of sensitive information

## Slide 21: WLAN Security “Visibility”
Prevalence of technology
  PWLAN (Public Wireless LAN) and other public 802.11 networks
Other security fears—identity theft, phishing, etc.
  “Hackers target Xbox Live players”, Feb 20, 2009
  http://news.bbc.co.uk/2/hi/technology/7888369.stm
  “Crime to boom as downturn blooms” Dec 30, 2008
  http://news.bbc.co.uk/2/hi/technology/7797946.stm
  Public availability of tools
  Aircrack—WEP key exploit
  coWPAtty—WPA-PSK exploit
  Kismac—MAC-based implementation of Kismet
  http://www.darknet.org.uk/2006/04/top-15-securityhacking-tools-utilities
Notes: 21
21

## Slide 22: Wireless Security Threats Classifying the attack types
Denial of Service
DENIAL OF SERVICE
Service disruption
Evil Twin/Honeypot AP
HACKER’S AP
Connection to malicious AP
Reconnaissance
Seeking network vulnerabilities
HACKER
Cracking Tools
Sniffing and eavesdropping
HACKER
On-Wire Attacks
Over-the-Air Attacks
Non-802.11 Attacks
Backdoor access
BLUETOOTH AP
RADAR
RF-JAMMERS
BLUETOOTH
MICROWAVE
Service disruption
Ad-hoc Wireless Bridge
Client-to-client backdoor access
HACKER
Rogue Access Points
Backdoor network access
HACKER
Notes: 22
With the value-add brought by WLANs, so too comes additional network threat possibilities. These fall into three main categories.
On-Wire Attacks: whether you have a wireless network or not, the threat of unsanctioned wireless devices, called ‘rogues’, is still very real. The key thing to understand here is that whatever a customer’s WLAN strategy, rogues may compromise wired network security by allowing rogue wireless clients access to network resources.
  Rogue APs: very simply, an unsanctioned AP that is connected to the wired network and offers up service to unsanctioned clients. These APs can be ‘open’ or have security employed (to both limit the unsanctioned users allowed to connect and help stay off administrators’ radars).
  Ad-hoc Wireless Bridges: a subset of the 802.11 protocol allows peer-to-peer connectivity, called ad-hoc networking. The main threat these networks pose is the possibility that machines connected to the wired network may be configured to also participate in such an ad-hoc connection, and the link between the two networks could then be bridged, thereby allowing unsanctioned wireless access to wired network resources. Windows and Mac wi-fi-enabled laptops can function as an ad-hoc bridge. In Windows and MAC OS’s the ad-hoc functionality is on by default, in fact.
Over-the-Air Attacks: any WLAN may be susceptible to both active and passive wireless attacks.
  Man-in-the-middle (Evil Twin, Honeypot AP, etc) Attacks: there are many types of these attacks, but all are based in the same exploit. An intruder inserts himself in between a legitimate client and the resources that client is attempting to access. This can be done between the client and the legitimate infrastructure, or by getting the client to connect to a rogue access point may serve as the means to provide visibility into sensitive traffic. Each attack takes aim at the same 802.11 vulnerability: unauthenticated management frames.
  Denial of Service (DoS) Attacks: there are myriad standards-based ways for interlopers to prevent sanctioned clients from accessing network resources. The vast majority of these attacks are simple exploits of unauthenticated management frames.
  Reconnaissance and Cracking: many passive or nearly passive recon tools exist to give administrators and hackers information on network configuration and topology. Cracking tools take that a step further and try to decipher wireless traffic, either on-the-fly or offline.
Non-802.11 Attacks: many technologies occupy (intentionally, or otherwise) the same spectrum that 802.11 networks use (2.4 and 5GHz).
  Backdoor Access: other networking technologies, such as Bluetooth, not only interfere with 802.11 (which can cause degradation of wireless network performance), but can be used to sacrifice the integrity of the wired network or devices. A Bluetooth AP can serve as a rogue AP just like an 802.11 AP.
  Service Disruption: a multitude of devices coexist in the same RF space as 802.11 networks and these devices can interfere with proper WLAN operation.

## Slide 23: WLAN Security Vulnerabilities and Threats
WLAN sniffing/war driving
Encryption vulnerabilities: WEP
Denial of Service (DoS) attacks: using 802.11 de-authentication/disassociation frames, RF jamming, etc.
Authentication vulnerabilities: dictionary attacks, MITM attacks
Address spoofing: MAC-address spoofing and IP address spoofing (both hostile/outsider attacks as well as insider attacks)
Examples of Existing Vulnerabilities and Threats
Notes: 23
23

## Slide 24: An Example: How Does a Wireless Exploit Take Place?
Probe response “listening” (to get SSID)
Passive WEP key sniffing
Initial phases of WLAN security exploit
  Discovery of WLAN networks by monitoring for probe/probe responses
  Collection of sufficient encrypted packets, offline processing and attempt to calculate WEP key
Notes: 24
24
SSID “cloaking” not really considered a security mechanism
(well known WEP exploits- rendered relatively obsolete with WPA)

## Slide 25: An Example: How Does a Wireless Exploit Take Place?
For example, “Kismac” tool: offers a “suite” of exploit tools with a easy-to-use GUI
http://www.ethicalhack.org/videos.php
Authentication exploits can then be undertaken, once a client has been provoked to re-authenticate
Or, if client may be induced to negotiate unauthenticated/unencrypted connection, a direct exploit on client may be undertaken
Active De-Auth to Induce Clients to Probe (Reduces Time to Overcome SSID “Cloaking”
Notes: 25
25
Use Screenshot from more advanced exploit tool, such as Auditor/Kismet/Kismac
Best Animation to show:
1) WLAN sniffing
2) Management frame exploit
3) Client connection solicitation
4) Potential client auth data harvest

## Slide 26: WLAN Sniffing and SSID Broadcasting
The Simplest Type of WLAN Exploit
However, given the “open” characteristics of 802.11 association behavior, one that is not easily fixed
Disabling SSID “broadcast” simply overcomes passive sniffing; SSID is easily discovered by observing probe responses from clients
Thus, SSID “cloaking” shouldn’t be considered a security mechanism
Notes: 26
26

## Slide 27: 802.11 WEP Vulnerabilities
802.11 Static-WEP is flawed: encryption passive attacks
  RC4 Key Scheduling algorithm uses 24-bit Initialization Vector (IV) and does not rotate encryption keys
  Practical tools that have implemented FMS attack (example: AirSnort) can uncover the WEP key after capturing 1,000,000 packets
  This is about ~ 17 minutes to compromise the WEP key in a busy network; this attack is passive and all the attack tool needs to do is “listen” to the WLAN network (i.e., sniff WLAN packets)
802.11 Static-WEP is flawed: encryption active attacks
  Does not protect the WLAN user data integrity
  Several forms of attacks possible: Replay attacks, bit-flipping attacks, etc.
802.11 Static-WEP shared key authentication is flawed
  AP challenges (plaintext challenge) the WLAN user to ensure possession of valid encryption key
  Attacker can obtain key stream  plaintext challenge XOR ciphertext = Key Stream
Notes: 27
27
FMS attack was discovered by Fluhrer, Mantin, and Shamir to utilize weak IVs and statistically derive WEP encryption key.
1,000,000 packets/ 1000 packets/sec = 1000 sec ~= 17 minutes {Note: AP’s max packet switching rate is about 1000 packets/second)

## Slide 28: Wireless: Man in the Middle Attacks
A MiTM is when an attacker poses as the network to the clients and as a client to the actual network
  Attacker must first force client off of intended network in order to lure wireless station to associate to “rogue network”
  The attacker gains security credentials by intercepting user traffic
Very easy to do with:
  MAC Address Spoofing
  Rogue Device Setup
  DoS Attacks
  Easier Sniffing, and war-driving

## Slide 29: Wireless: Rogue Devices
What is a Rogue?
  Any device that’s sharing your spectrum, but not managed by you
  Majority of rogues are setup by insiders (low cost, convenience, ignorance)
When is a Rogue dangerous?
  When setup to use the same ESSID as your network (honeypot)
  When it’s detected to be on the wired network too
  Ad-hoc rogues are arguably a big threat, too!
  Setup by an outsider, most times, with malicious intent
What needs to be done?
  Classify
  Detect
  Reporting, if needed
  Track (over-the-air, and on-the-wire) and Mitigate (Shutdown, Contain, etc)

## Slide 30: Rogue AP Vulnerability: Both Internal and External Sources
Frustrated insider
User that installs wireless AP in order to benefit from increased efficiency and convenience it offers
Common because of wide availability of low cost APs
Usually ignorant of AP security configuration, default configuration most common
Malicious hacker
Penetrates physical security specifically to install a rogue AP
Can customize AP to hide it from detection tools
Hard to detect—more effective to prevent via 802.1x and physical security
More likely to install LINUX box than an AP
James from Accounting
Most Rogue APs
Less likely
Notes: 30
30

## Slide 31: What Is a Dictionary Attack Tool?
What is a dictionary?
  Contains variations of passwords
  Weak passwords can be cracked using standard dictionaries (found easily in various Internet discussion forums and web sites)
Success factors for this tool depend on:
  Variation of the user’s password must be found in the dictionary used by the attacker
  Attacker’s experience and knowledge in generating dictionaries
  Password strength
    A weak six character password will be easily compromised compared to a strong ten letter password
    Attacker’s dictionary strength determines whether the password can be compromised
Notes: 31
31

## Slide 32: MAC Address Spoofing
As with wired networks, MAC address and IP address spoofing are possible, if not easy, in Wireless Networks
Outsider (hostile) attack scenario
  Does not know key/encryption policy
  IP Address spoofing is not possible if Encryption is turned on (DHCP messages are encrypted between the client and the AP)
  MAC Address spoofing alone (i.e., without IP Address spoofing) may not buy much if encryption is turned on
Insider attack scenario
  Seeking to obtain users’ secure info
  MAC address and IP Address spoofing will not succeed if EAP/802.1x authentication is used (unique encryption key is derived per user (i.e., per MAC address))
Authorized Client
Sniff Client MAC Addr and IP Address
Inject Packets into the WLAN Network Using Client’s MAC/IP Address
Access Point

## Slide 33: Wireless Sniffing: Good and Bad
First – Sniffing, or capturing packets over the air, is an extremely useful troubleshooting methodology
Sniffing, in the old days was reliant on very specific cards and drivers
Very easy to find support for most cards and drivers today
Cost (if you like to pay for it) of such software is negligible (or, just use free/opensource software)
Provides an insight (with physical proximity) into the network, services, and devices which comes in handy when performing network reconnaissance

## Slide 34: WLAN Security Denial of Service Attacks
RF Jamming
  Any intentional or un-intentional RF transmitter in the same frequency can adversely affect the WLAN
DoS using 802.11 Management frames (MPF can help mitigate)
  Management frames are not authenticated today
  Trivial to fake the source of a management frame
  De-Authentication floods are probably the most worrisome
Misuse of Spectrum (CSMA/CA – Egalitarian Access!)
  “Silencing” the network with RTS/CTS floods, Big-NAV Attacks
802.1X Authentication floods and Dictionary attacks
  Overloading the system with unnecessary processing
  Legacy implementations are prone to dictionary attacks, in addition to other algorithm-based attacks
Notes: ‘B’ key
Talk about that tools can be used off the shelf
Backtrack Live CDs
If you want to check these out, use a Cisco CB21-AG (Atheros based) and a backtrack live cd.

## Slide 35: Authentication Vulnerabilities
Management frames are not authenticated !
Dictionary attacks
  On-line (active) attacks: active attack to compromise passwords or pass-phrases
  Off-line attacks: passive attack to compromise passwords or pass-phrases
MITM attacks
  Active attacks: an attacker attempts to insert himself in the middle of authentication sequence
Can be employed in 802.1X as well as PSK environments
  Multiple known WEP weaknesses, and many exploits out there

## Slide 36: Exploits Using 802.11 as a Launchpad
Standard Layer 2 exploits, e.g., Dsniff, Nmap
Penetration test—server and service vulnerabilities:
  Metasploit project—open source RPC injector http://metasploit.com
  Immunity CANVAS
  Core security technology impact
Application security—exploit/malware
Specific examples that have been launched:
  Installation of various viruses, worms, and other malware, thereby complicating detection—Security Conference, Canfield University, UK
  Simple sniffing of unencrypted user ID, passwords, account nos., etc.—Wi-Fi hotspots
Notes: 36
36
Malware- viruses/worms, spyware, Trojan horses, adware
Note difference between server/service and application security:
  SQL injection, form/field manipulation, cookie tampering
  Dsniff is a passive sniffer
  Nmap is a free security scanner written by Fyodor. It is used to evaluate the security of computers, and to discover services or servers on a computer
  Immunity CANVAS is groundbreaking software that allows you to test compliance and let your organization discover how vulnerable you really are

## Slide 37: WLAN Security Vulnerabilities and Threats Summary
Wireless LANs have become easy targets for both “traditional” network exploits, as well as criminal element
Passive SSID probe sniffing and WEP key attacks are just the first stage in WLAN exploits
More sophisticated WLAN exploits are likely to employ management frames, as there is currently no encryption capable for these 802.11 media management packets
If an attacker can gain access to a WLAN, it is possible to launch a variety of higher-layer exploits over this media
Notes: 37
37

## Slide 38: Quick Look: Common WLAN Exploits/Tools
Remote-Exploit/Backtrack/Auditor
Aircrack, WEPcrack, etc
coWPAtty
Kismet
NetStumbler, Hotspotter, etc
AirSnort
Sniffing tools: OmniPeek, Wireshark
dsniff, nmap
wellenreiter
asleap

## Slide 39: Over-the-Air Attack Techniques and Tools
Network Profiling and Reconnaissance
Authentication and Encryption Cracking
Honeypot AP
Netstumbler
Man-in-the-Middle
Denial of Service
Dictionary attacks
AirSnarf
Hotspotter
WEPCrack
MAC/IP Spoofing
Fake AP
Malformed 802.11 frames
FATA-Jack, AirJack
Fragmentation attacks
Excessive authentication
De-auth attacks
Association attacks
CTS attacks
RTS attacks
Excessive device bandwidth
Kismet
Wellenreiter
Excessive device error
Excessive multicast/broadcast
ASLEAP
EAP-based attacks
CoWPAtty
Chop-Chop
Airckrack
Airsnort
PSPF violation
WEP Attack
Illegal frame types
Excessive association retries
Excessive auth retries
LEAPCracker
Fake DHCP server
Pre-standard APs (a,b,g,n)
EAPOL attacks
Probe-response
Resource management
RF Jamming
Michael
Queensland
Virtual carrier
Big NAV
Power-save attacks
Microwave interference
Bluetooth interference
Radar interference
Other non-802.11 interference
Device error-rate exceeded
Interfering APs
Co-channel interference
VoWLAN-based attacks
Excessive roaming
Evil Twin AP
ARP Request Replay Attack
Notes: 39
This slide shows examples of the different classes of over-the-air attacks we detect. It is not meant to be a comprehensive slide, but more of an illustration of the attack detection breadth we have.
See the wIPS product collateral page on CEC for a document with a complete list of attacks detected. It’s changing all the time as we add more detection capabilities.

## Slide 40: Threat Mitigation Technologies

## Slide 41: Cisco’s Attack Detection Mechanisms
Base IDS
Built-in to Controller Software
Uses Local and Monitor Mode APs
Adaptive wIPS
Requires MSE
Uses wIPS Monitor Mode and/or Local APs

## Slide 42: Cisco Wired IPS Integration Unified Intrusion Prevention
Client Shun
Inspects traffic flow for harmful applications and blocks wireless client connections
Layer 3-7 Deep Packet Inspection
Eliminates risk of contamination from wireless clients
Zero-day response to viruses, malware and suspect signatures
http://www.cisco.com/en/US/tech/tk722/tk809/technologies_configuration_example09186a008080dc8c.shtml
Enterprise Intranet
Cisco ASA w/ IPS
L2 IDS
Malicious Traffic
Mitigate Network Misuse, Hacking and Malware from WLAN Clients
Business Challenge
L3-7 IDS
Notes: 42
42

## Slide 43: What is CleanAir?
Detect and Classify
Cisco CleanAir
High-resolution interference detection and classification logic built-in to Cisco’s 802.11n Wi-Fi chip design. Inline operation with no CPU or performance impact.
100
63
35
97
90
20
Uniquely identify and track multiple interferers
Detects security-risk interferers like RF Jammers and Video Camera.
Assess unique impact to Wi-Fi performance
Monitor AirQuality
43
Notes: The detection and classification of interference sources is part of the advanced chipset design of the access point. This allows the access point to uniquely classify many sources of interference including microwave ovens, jamming devices, bluetooth, gaming devices, cordless phones and spy cams – to name a few.

## Slide 44: Management Frame Protection Concept
Wireless management frames are not authenticated, encrypted, or signed
A common vector for exploits
Insert a signature (Message Integrity Code/MIC) into the management frames
Clients and APs use MIC to validate authenticity of management frame
APs can instantly identify rogue/exploited management frames
Infrastructure MFP Protected
Client MFP Protected
Disassociation
AP Beacons | Probe Requests/ Probe Responses
Associations/Re-associations | Disassociations
Authentications/ De-authentications | Action Management Frames
Problem
Solution
CCXv5
Notes: 44
44

## Slide 45: WLAN Security Vulnerabilities and Threats
Denial of Service
DENIAL OF SERVICE
Service disruption
Ad-hoc Wireless Bridge
Client-to-client backdoor access
HACKER
Rogue Access Points
Backdoor network access
HACKER
Evil Twin/Honeypot AP
HACKER’S AP
Connection to malicious AP
Reconnaissance
Seeking network vulnerabilities
HACKER
Cracking Tools
Sniffing and eavesdropping
HACKER
On-Wire Attacks
Over-the-Air Attacks
Non-802.11 Attacks
Backdoor access
BLUETOOTH AP
RADAR
RF-JAMMERS
BLUETOOTH
MICROWAVE
Service disruption
Cisco wIPS Detects These Attacks
Cisco CleanAir Detects These Attacks
Notes: 45
As previously outlined, the network is able to detect all the above attacks…
  but, add an ounce of prevention, and there’s more….

## Slide 46: WLAN Security Vulnerabilities and Threats
Denial of Service
DENIAL OF SERVICE
Service disruption
Ad-hoc Wireless Bridge
Client-to-client backdoor access
HACKER
Rogue Access Points
Backdoor network access
HACKER
Evil Twin/Honeypot AP
HACKER’S AP
Connection to malicious AP
Reconnaissance
Seeking network vulnerabilities
HACKER
Cracking Tools
Sniffing and eavesdropping
HACKER
On-Wire Attacks
Over-the-Air Attacks
Non-802.11 Attacks
Backdoor access
BLUETOOTH AP
RADAR
RF-JAMMERS
BLUETOOTH
MICROWAVE
Service disruption
Cisco wIPS Detects These Attacks
Cisco CleanAir Detects These Attacks
Rogue detection, classification and mitigation addresses these attacks
MFP Neutralizes all Management Frame Exploits, such as Man-in-the-Middle Attacks
WPA2/802.11i Neutralizes Recon and Cracking Attacks
Notes: 46
As previously outlined, the network is able to detect all the above attacks…
  but, add an ounce of prevention, and there’s more….

## Slide 47: Strong Authentication and Encryption

## Slide 48: 802.11 Security Fundamentals: Setting up a secure 802.11 link
Authentication
  Enforce strong, mutual authentication of client & server
  Recommendation is 802.1X/EAP
  802.1X blocks user access until authentication successful
Association
  Establish a virtual port for the link
Encryption
  Enforce strong encryption to provide data privacy over the 802.11 link
    Recommendation is AES (WPA2) or TKIP (WPA)
AAA
Server
Notes: EAP = Extensible Authentication Protocol
AES = Advanced Encryption Standard
TKIP = Temporal Key Integrity Protocol

## Slide 49: Secure or open SSID?
Secure SSID
Open SSID
A secure SSID cannot fall back to open.
  Example: users not supporting 802.1X cannot fall back to web portal authentication on the same SSID as corporate users.
Pre-shared keys (PSK) and keys derived from 802.1X cannot co-exist on a secure SSID.
On both types of SSIDs you can combine multiple identity services if needed.
  Examples: guest users going through posture assessment, employees going through MDM, employees going through web portal after device authentication, etc.

## Slide 50: Authentication Evolution
WEP
802.1x / Dynamic WEP
WPA/WPA2
MAC Address Authentication
Notes: Move towards WPA/WAP2

## Slide 51: WPA/WPA2 Breakdown
WPA
A Snapshot of the 802.11i Standard
WPA2
Final Version of 802.11i
Commonly Used with AES Encryption
Authentication
Mechanisms
Personal (PSK) – Home Use
Enterprise (802.1x/EAP) – Office Use
Commonly Used with TKIP Encryption

## Slide 52: Authentication: Open

## Slide 53: Authentication: PSK (WEP)

## Slide 54: Authentication: PSK (WEP) (Cont.)
  WLAN security protocol defined in the 802.11 specification:
    Operates at Layer 2 and does not offer end-to-end security
  Uses key plus initialization vector:
    Initialization vector is a random number generated through the WEP algorithm
    Key and initialization vector are used in encryption of the data
  Three user-specified key lengths:
    40-bit key, combined with initialization vector to yield 64 bits
    104-bit key, combined with initialization vector to yield 128 bits
    128-bit key, combined with initialization vector to yield 152 bits
  Cisco wireless supports pre-shared key authentication:
    Disabled by default

## Slide 55: WEP Limitations
  No per-packet authentication or message integrity check
  Hackers can easily obtain challenge phrase and encrypted response:
    Crack the WEP key
    Correctly decrypt captured data traffic
  Weak encryption of data
  Repeating initialization vector can provide insight into cracking WEP key
  Each client and AP must be configured with matching WEP key
  Managing keys can be difficult in enterprise WLAN
  Less secure than using open Layer 2 association and then applying user authentication with dynamic encryption method

## Slide 56: Wi-Fi Protected Access (WPA)
  WPA introduced in late 2003
  Pre-standard implementation of IEEE 802.11i WLAN security
  Addresses currently known security problems with WEP
  Allows software upgrade on already deployed 802.11 equipment to improve security
  Components of WPA
    Authenticated key management using 802.1X: EAP authentication, and PSK authentication
    Unicast and broadcast key management
    Standardized TKIP per-packet keying and MIC protocol
    Initialization vector space expansion: 48-bit initialization vectors
    Migration mode—coexistence of WPA and non-WPA devices (optional implementation that is not required for WPA certification)

## Slide 57: WPA Authentication Modes
Enterprise (802.1X Authentication) | Personal (PSK Authentication)
Authentication server required | Authentication server not required
RADIUS used for authentication and key distribution | Shared secret used for authentication
Centralized access control | Local access control
Encryption uses TKIP, AES optional | Encryption uses TKIP, AES optional

## Slide 58: WPA2 and IEEE 802.11i
  802.11i
    Ratified in June 2004
    Standardizes
      802.1X for authentication
      AES to be used for encryption
      Key management
  WPA2
    Supplement to WPA ”version 1”, which uses TKIP encryption
    Provides for AES encryption to be used
    Third-party testing and certification for WLAN device compatibility

## Slide 59: IEEE 802.11i and AES Encryption
Uses AES encryption in lieu of RC4 encryption
  Specific AES implementation used in 802.11i is called
  “AES Counter Mode with CBC-MAC authentication” (a.k.a. AES-CCMP)
  128-bit, symmetric block cipher (versus RC4 stream cipher)
  AES cryptographically more robust than RC4 (and requires more computational power)
  AES is implemented in hardware

## Slide 60: WPA/WPA2/802.11i Comparison
WPA | WPA2 | 802.11i
SOHO | Enterprise | Enterprise
802.1X authentication/PSK | 802.1X authentication/PSK | 802.1X authentication
128-bit RC4 w/ TKIP encryption cipher | 128-bit AES encryption cipher | 128-bit AES encryption cipher
Ad hoc not supported | Ad hoc not supported | Allows ad hoc
Test devices for compliance | Test devices for compliance | No test, specification

## Slide 61: MAC Filtering
  Allows clients based on their MAC addresses
  The option is enabled on a per WLAN basis
  Controller checks for the presence of the client MAC address:
    In a local database
    If the address is not present, relays to a RADIUS server
  Local list contains 500 addresses, can be extended to 2000
    The database is shared by local management users (including lobby ambassadors), net users (including guest users), MAC filter entries, and disabled clients.

## Slide 62: Choosing an EAP Method
EAP Type(s) Deployed
Client Support
Security vs. Complexity
Authentication Server Support
Most clients such as Windows, Mac OSX, Apple iOS devices support EAP-TLS, PEAP (MS-CHAPv2).
  Additional supplicants can add more EAP types (Cisco AnyConnect).
Certain EAP types (TLS) can be more difficult to deploy than others depending on device type.

## Slide 63: Authentication Best Practices: WPA2-Enterprise
Strong Authentication
Extensible Authentication Protocol (EAP)
Outside Methods (Protective Tunnel):
PEAP
EAP-FAST
Inside Methods (Authentication Credentials):
EAP-MSCHAPv2
EAP-GTC
AES
Strong Encryption
EAP-TLS (Certificate Based)

## Slide 64: EAP Authentication Types
Tunneling-Based
EAP-PEAP
EAP-TTLS
Inner Methods
EAP-GTC
EAP-MSCHAPv2
EAP-FAST
Tunnel-based - Common deployments use a tunneling protocol (EAP-PEAP) combined with an inner EAP type such as EAP-MSCHAPv2.
  This provides security for the inner EAP type which may be vulnerable by itself.
Certificate-based – For more security EAP-TLS provides mutual authentication of both the server and client.
Certificate-Based
EAP-TLS

## Slide 65: EAP Methods Comparison
 | EAP-TLS | PEAP | EAP-FAST
Fast Secure Roaming (CCKM) | Yes | Yes | Yes
Local WLC Authentication | Yes | Yes | Yes
OTP (One Time Password) Support | No | Yes | Yes
Server Certificates | Yes | Yes | No
Client Certificates | Yes | No | No
PAC (Protected Access Credentials)* | No | No | Yes
Deployment Complexity | High | Medium | Low
* PACs can be provisioned anonymously for minimal complexity.

## Slide 66: Encryption Evolution
TKIP
(RC4 and MIC)
AES
(CCMP)
WEP (RC4)
Notes: WEP, static keys, RC4 algorithm, no message integrity check
TKIP, RC4 with rotating keys, avoiding the whole weak IV problem, included a MIC
AES, which completely changes it around integrated MIC and key management, with a 128bit AES key

## Slide 67: Encryption Best Practices: TKIP and AES
TKIP (Temporal Key Integrity Protocol)
AES (Advanced Encryption Standard)
Use only for legacy clients without AES support
Often a software update for WEP clients
Requires hardware support (~2005 chipsets or later)
Achieves line-rate speeds
Only encryption standard supported for 802.11n data rates
Can be run in conjunction with AES (mixed-mode)
Is being discontinued by the WiFi Alliance for certification.

## Slide 68: The TKIP Vulnerability
Once thought safe, TKIP encryption is cracked: http://www.pcworld.com/businesscenter/article/153396/once_thought_safe_wpa_wifi_encryption_is_cracked.html
Security researchers claim that they can crack the message integrity (MIC) key used in TKIP
Recovery of MIC key facilitates packet forgeries, but only between AP and client
Encryption key is *not* recovered, therefore data traffic cannot be read via this attack – this is not like the WEP crack of years back
What is the Risk?
  Common traffic types, such as ARP and DNS, can be replayed to client for very limited duration… at most 7 times

## Slide 69: Centralizing WLAN Authentication

## Slide 70: 802.1x
WLC

## Slide 71: 802.1x Architecture
EAP
Session Key
Microsoft
Microsoft/
Cisco/
RSA
Encryption
Authentication
Credentials
Cisco
Username and Password
Certificate
EAP-Fast
TLS
PEAP
PEAP
WPA
WPA2
802.1x
TKIP
AES
WEP
Notes: 71
71
Transcript:
The 802.1x architecture includes these Layer 2 policies for protecting network access: It is an IEEE standard covering port-based access control for controllers. 802.1x authentication takes place following AP association. It provides better security than Layer 2 802.11 authentication. It uses EAP. EAP was originally defined as a PPP protocol (RFC 2284) and was adapted by the IEEE. It provides a variety of authentication methods. And finally, it becomes EAP over LAN (EAPOL) in an 802.1x context. EAP-PEAP-MS-CHAPv2 is a common authentication method used for 802.1x security.
Author’s Original Notes:
The 802.1x architecture includes these Layer 2 policies for protecting network access:
It is an IEEE standard covering port-based access control for controllers.
802.1x authentication takes place following AP association.
It provides better security than Layer 2 802.11 authentication.
It uses EAP.
  EAP was originally defined as a PPP protocol (RFC 2284) and was adapted by the IEEE.
  It provides a variety of authentication methods.
  And finally, it becomes EAP over LAN (EAPOL) in an 802.1x context.

## Slide 72: 802.1x Identity Information Types
Different types for different mobility use cases:
1. Username/Password Combination
  User authentication (also Machine Auth for Windows)
  Active Directory/LDAP/RADIUS ID Stores
  EAP types: PEAP-MSCHAPv2, PEAP-GTC, EAP-FAST
2. Two-Factor Authentication
  Something you know, you have, you are
  Mostly for user authentication
  RSA SecurID and other token-based ID Systems
  EAP types: PEAP-GTC, EAP-FAST/EAP-GTC
3. Digital Certificates
  Signed/emitted by a public or private Certificate Authority
  Can be used for user and/or device authentication
  Microsoft AD Certificate Services, Entrust, Verisign, etc.
  EAP types: EAP-TLS, EAP-FAST
EAP
Extensible Authentication Protocol
PEAP
Protected EAP
GTC
Generic Token Card
FAST
Flexible Authentication
via Secure Tunneling
TLS
Transport Layer Security

## Slide 73: Local EAP
  The following EAP methods are supported with local EAP:
    LEAP
    EAP-FAST (both username and password with PAC and certificates)
    EAP-TLS
    PEAP
  MAC authentication is also supported in addition to the above methods
  Local EAP authentication can be used if the Cisco WLC fails to reach the configured RADIUS servers
  Supports local users or LDAP users
  Requires WLAN configuration

## Slide 74: LEAP
  Cisco WLAN security solution
  User authentication via user ID and password
  Single login using Windows NT/2000 Active Directory
  Dynamic WEP keys and mutual authentication
    Key integrity protocol/message integrity recommended
  Simplified deployment and administration
  Supports multiple operating systems
    Windows, Mac OS, Windows CE, DOS, and Linux
  Strong password policy recommended

## Slide 75: EAP-FAST
Considered in three phases:
  Protected Access Credentials (PAC) is generated in phase zero (Dynamic PAC provisioning)
    Unique shared credential used to mutually authenticate client and server
    Associated with a specific user-ID and an Authority ID
    Removes the need for PKI
  A secure tunnel is established in phase one
  Client is authenticated via the secure tunnel in phase two

## Slide 76: EAP-TLS
  Client support
  Windows 2000, XP, Vista and Windows CE (natively supported)
  Linux, Mac AirPort Extreme
  Each client requires a user certificate
  Infrastructure requirements
  EAP-TLS-supported RADIUS server
  RADIUS server requires a server certificate
  Certificate Authority server (PKI Infrastructure)
  Certificate management
  Both client and RADIUS server certificates to be managed

## Slide 77: PEAP
  Hybrid authentication method
    Server side authentication with TLS
    Client side authentication with EAP authentication types
      EAP-GTC
      EAP-MSCHAPv2
  Clients do not require certificates
  RADIUS server requires a server certificate
    RADIUS server self-issuing certificate capability
    Purchase a server certificate per-server from public PKI entity
    Setup a simple PKI server to issue server certificates
  Allows for one-way authentication types to be used
    One-time passwords
    Proxy to LDAP, Unix, Microsoft NT and Active Directory, Kerberos

## Slide 78: CCX—Providing Security Alternatives/ Tools/Cross-Platform Compatibility
CCX v5
MFP
Client policies/ reporting
CCX v1
802.1x authentication
EAP-TLS and LEAP
Cisco pre-standard TKIP
Client rogue reporting
CCX v2
WPA compliance
Fast roaming with CCKM
PEAP
CCX v3
WPA2 compliance
EAP-FAST
CCKM with EAP-FAST
AES encryption
CCX v4
CCKM with EAP-TLS, PEAP
WIDS
MBSSID
More Than Just Standards

## Slide 79: EAP Protocols: Feature Support
 | EAP-TLS | PEAP | LEAP | EAP-FAST
Single Sign-on | Yes | Yes | Yes | Yes
Login Scripts (MS DB) | Yes1 | Yes1 | Yes | Yes
Password Expiration (MS DB) | N/A | Yes | No | Yes
Client and OS Availability | Vista, XP, CE, and Others2 | Vista, XP, CE, CCXv2 Clients3, and Others2 | Cisco/CCXv1 or Above Clients and Others2 | Cisco/CCXv3 Clients4 and Others2
MS DB Support | Yes | Yes | Yes | Yes
LDAP DB Support | Yes | Yes5 | No | Yes
OTP Support | No | Yes5 | No | Yes6
1 Windows OS supplicant requires machine authentication (machine accounts on Microsoft AD)
2 Greater operating system coverage is available from via CSSC and third party supplicants
3 PEAP/GTC is supported on CCXv2 clients and above
4 Cisco 350/CB20A clients support EAP-FAST on MSFT XP, 2000, and CE operating systems EAP-FAST supported on CB21AG/PI21AG clients with ADU v2.0 and CCXv3 clients
5 Supported by PEAP/GTC only
6 Supported with 3rd party supplicant
Notes: 79

## Slide 80: EAP Protocols: Feature Support
 | EAP-TLS | PEAP | LEAP | EAP-FAST
Off-Line Dictionary Attacks? | No | No | Yes1 | No
Local Authentication | No | No | Yes | Yes
WPA Support | Yes | Yes | Yes | Yes
Application Specific Device (ASD) Support | No | No | Yes | Yes
Server Certificates? | Yes | Yes | No | No
Client Certificates? | Yes | No | No | No
Deployment Complexity | High | Medium | Low | Low
RADIUS Server Scalability Impact | High | High | Low | Low/Medium
1 Strong password policy mitigates dictionary attacks; please refer to: http://www.cisco.com/en/US/products/hw/wireless/ps430/prod_bulletin09186a00801cc901.html
Notes: 80

## Slide 81: Web Authentication
  This allows users to authenticate through a web interface
  Clients who attempt to access the WLAN using HTTP are automatically directed to a login page:
    Login page is customizable for logos and text
    Maximum simultaneous authentication requests using web authentication is 21
    Maximum number of local web authentication users is 2048 (default 512)
  This is generally used for guest access
  The Login page on the controller is now fully customizable

## Slide 82: Web Authentication Page Configuration
Default Login Page
Customized Login Page (based on the previous slide’s configurations and a custom logo uploaded to the controller)
Notes: Transcript:
Using your own content, including HTML tags, in the Title and Message boxes, and customized logos uploaded to the controller, you can create a customized web authentication login page on the controller, without having to use an external web server. To further customize the web authentication page on the controller, you can upload a completely customized html page and images bundled into a .tar file, known as a web auth bundle, to the controller. See the Cisco Wireless LAN Controller Configuration Guide for details on this process. For extremely customized login pages, you may also choose to redirect users to an external web server for authentication rather than using the controller itself.
Author’s Original Notes:
Using your own content (including HTML tags) in the Title and Message boxes, and customized logos uploaded to the controller, you can create a customized web authentication login page on the controller, without having to use an external web server.
To further customize the web authentication page on the controller, you can upload a completely customized html page and images bundled into a .tar file (known as a webauth bundle) to the controller. See the Cisco Wireless LAN Controller Configuration Guide for details on this process.
For extremely customized login pages, you may also choose to redirect users to an external web server for authentication rather than using the controller itself.

## Slide 83: Conclusion/Remarks/Resources

## Slide 84: Conclusion / Remarks
When Deploying Wireless Networks… Security should always be the primary concern.
Deploy WLAN Security with a MINIMUM security configuration of WPA2/PSK and AES Encryption.
Guest Wireless Access should adhere to the MINIMUM security configuration, but in the event that is not feasible, use WebAuth with a Splash Page and disclaimers and a Login.
Enterprise WLAN Deployments should ALWAYS separate Guest Access and Corporate Access with WVLANs and separate SSIDs.
WLANs are always being scanned… Be aware and monitor your RF environment.

## Slide 85: Resources
The Cisco Learning Network
  https://learningnetwork.cisco.com/welcome
  CCNA Wireless Study Materials
  https://learningnetwork.cisco.com/community/certifications/wireless_ccna/wifund/study-material
  CCNA Wireless Certification Exam Topics
  https://learningnetwork.cisco.com/community/certifications/wireless_ccna/wifund/exam-topics