Дробеструйная линия 1200 mm ширина

- Price List

| No. | Name | Qty | Specification | Unit Price (USD/SET) |
| --- | --- | --- | --- | --- |
| 1 | Shot Blasting Assemble | 4 | Shot blasting device, motor, motor seat, ingress pipe, vane wheel, vanes, protective plates, combined discs, sand retaining discs, transmission mechanisms, etc. |  |
| 2 | Shot cabinet | 1 | Steel structure chamber body, projectile zone combined guard plate, alloy steel cap, protective belt, etc. |  |
| 3 | Seal Room | 1 | Steel structure room body, observation door, sealing curtain, rubber protective plate, etc. |  |
| 4 | Roller Converyor Structure | 1 | Sprocket chain, bearing, driving mechanism, tensioning mechanism, wear-resistant roller table of shot blasting chamber, sheath, sealed chamber roller table, outdoor roller table, sprocket cover, etc. |  |
| 5 | Shot and residue separator | 1 | Winnowing mechanism, spiral distributor, air volume regulating valve, tightening mechanism, pellet storage hopper, filter and other devices. |  |
| 6 | Spiral conveyor | 2 | body, screw shaft and support, 16Mn blades, reducer drive mechanism, sealing device |  |
| 7 | Bucket type elevator | 1 | Head drive mechanism, tail drive mechanism, tension mechanism, housing, belt, hopper, bearing, etc. |  |
| 8 | Shot feeding system | 4 | Projectile controller, polyurethane pill supply tube |  |
| 9 | Shot blowing system | 1 | High-pressure fan, blowpipe, etc. |  |
| 9 | Electrical control system | 1 | Control cabinets, inverters, cables, electrical materials, bridges, gas control boxes, pulse controllers, etc. |  |
| 10 | Dust Clean System | 1 | Settlement chamber, dust collector assembly, fan, pipeline, etc. |  |
| 12 | Random spare parts |  | 4 pieces of directional sets, 4 pieces of pill wheel, 4 groups of blades |  |
| 14 | Total |  | USD/SET | 36000 USD |

Price Term: FOB QINGDAO PORT.

Validity: Before 2021-12-20

Доставка 40 футовий HC контейнер + 26% МИТО/ПДВ

- Main Parameter For Full Line

| Item | Unit | Value |
| --- | --- | --- |
| Overall size | mm (L×W×H) | As per drawing |
| Shot-blast cabinet input size | mm W×H | 1100×300 |
| Useful Processing Size | mm (L×W×H) | 4000x800x20mm |
| Max. Weight of workpiece | KG | 500 |
| Processing speed | m/min | 1.0-2.0 |
| Roughness of surface | μ | 40~85（Depends on shot size） |
| Power | kw | About 70KW |
| Air consumption | m³/min | 0.2 |
| Air Pressure | MPa | 0.5-0.7 |
| Control system |  | PLC, by switch |
| Noisy（measure outside factory） | dB | ≤95 |
| Dust Density | mg/m3 | 120mg/m3 |
| Dust content in air after cleaning | mg/m3 | 10 |

- Shot Parameter

| Item | Unit | Value |
| --- | --- | --- |
| Shot carbinet body | Steel |  | Q235 |
|  | Friction preserved body |  | Rolling manganese 13 |
| Shot Device | Model |  | Q034ZZ |
|  | Vane |  | Double round disk stright line |
|  | Shot quantity/carbinet | kg/min | 180 |
|  | Power/set | kw | 11 |
|  | Quantity | pcs | 4 |
|  | Shot blasting speed | m/s | 76 |
| Shot recycle system | Spiral conveyor | Shot convey speed | T/H | 45 |
|  |  | Dia of Spiral | mm | 300 |
|  |  | Power | kW | 2×2.2 |
|  |  | Quantity | set | 2 |
|  | Shot andsand separator | Separator quantity | T/H | 45 |
|  |  | Separator fan speed | M/S | 4—5 |
|  |  | Separator waste ratio |  | ≤1% |
|  |  | Quantity | set | 1 |
|  | Lifter | Lifting quantity | T/H | 45 |
|  |  | Lifting speed | M/S | 1.21 |
|  |  | Power | kW | 4 |
|  |  | Quantity | set | 1 |
| Shot control system | Spot | Dia | mm | φ0.2∽2.5 |
|  |  | Material |  | Steel cut wire shot、Cast steel alloy shot, etc. |
|  | Shot first loading quantity | kg | ≈4000 |
|  | Max. Flow rate for shot brake valve | Kg/min | 500 |
|  | Shot consumption | kg/m2 | 0.0075(Steel cut wire shot for example) |

4. Roller System Parameter:

| Item | Unit | Value |
| --- | --- | --- |
| Dynamic load | KG/M | 1000 |
| Total conveyor length | mm | 9500 |
| Distance of Roller | mm | 300 |
| Dia of roller | mm | 76 |
| Moving Speed(frequency control) | m/min | 0.1-4 |
| Total Power | kw | 2.2 |

5. Clean System

| Item |  | Unit | Value |
| --- | --- | --- | --- |
| Strong Sand blowing device | High Pressure Fan |  | 9-19-4.5A |
|  | Full Pressure | pa | 4684 |
|  | Blow Rate | m³/h | 1939 |
|  | Power | kw | 7.5 |
|  | Quantity | 台 | 1 |

- Dust Remover System

| Item | Unit | Value |
| --- | --- | --- |
| Dust Remover System | Fan Model |  | 4-72NO.5A |
|  | Fan Power | kw | 15 |
|  | Power of Dust Remover |  | ＞99.2％ |
|  | Full Pressure | pa | 1820 |
|  | Dedusting air volume | m³/h | 14800 |

Description:

- Main Assemble：

Roller Type Shot Blasting And Cleaning Production Line is combined by Shot Blasting Assemble, Shot Cabinet, Shot Recycle System(shot and residue separator,

- Shot blasting room

The shell of the shot blasting room is made of steel plate and section steel welding structure, which is a strong, sealed and spacious operating space for shot blasting of the workpiece.

The shot blasting cleaning chamber is composed of a chamber body shell, left and right side walls, rear side walls, top plate, guard plate and so on. The shot blasting room is equipped with 4 sets of Q034ZZ high-efficiency shot blasting assembly, and the reasonable layout of the ejection belt ensures that the cleaned workpieces are fully shot blasted. The projectile area in the chamber is protected by rolling Mn13, all guard plates are assembled by building blocks, and the guard plates in the chamber are all fixed on the cleaning chamber wall with wear-resistant cast iron nuts for compaction, which is convenient for disassembly and replacement. Extend the service life, reduce the cost of use, and reduce the frequency of maintenance. The inlet and outlet of the shot blasting chamber are equipped with sealed chambers, and the sealed chambers are hung with 4 layers of wear-resistant rubber curtains.

- Shot blasting assembly

The shot blasting device assembly is composed of shot blasting shell, motor, introduction pipe, blade, impeller, directional sleeve, blasting wheel, sand retaining plate, guard plate, etc., among which wear parts such as blades and guard plates are all made of chromium. Made of 20% high chromium wear-resistant cast iron

(American steel standard code: 5115G51150 model), all wearing parts are the most common national standard parts in the market.

In order to make the projectile uniformly atomized and hit the steel in an all-round way, the machine adopts a double-disc linear blade structure.

- Shot recycling purification system

The pill recycling purification device used in this machine includes a recycling system and a pill separation purification system, consisting of a screw conveyor, a bucket elevator, a pill sand separator, a pill supply gate valve, and a pill delivery pipe.

- Screw conveyor:

The screw conveyor is composed of a cover, a screw shaft, a bearing with a seat, a drive mechanism, etc. It is a series of parts of our company, with high versatility, interchangeability, and stable and reliable performance.

This part is responsible for conveying the shot-sand mixture to the elevator. The screw conveyor is located at the bottom of the shot blasting room, and the screw blades are welded on the drive shaft. When working, the conveyor motor drives the screw conveyor to rotate through the cycloid reducer to transport the pellets to the discharge port, and then the discharge port transfers the scattered pellets and dust mixture to the bottom of the elevator.

Both ends of the screw conveyor are protected by a three-level seal, a labyrinth seal is added inside the end plate, an oil seal is used for protection in the middle, and the bearing is isolated from the end plate on the outside of the end plate. Once the pellets and dust are squeezed out, they will fall from the gap between the end plate and the bearing and will not enter the bearing.

- Bucket elevator:

The bucket elevator is composed of a cycloid pinwheel reducer, upper and lower rollers, conveyor belt, hopper, closed barrel and tensioning device, etc., and the material is discharged by centrifugal gravity.

When working, the hopper fixed on the conveyor belt scrapes up the pellets at the bottom and sends the pellets to the top, and then falls by centrifugal gravity. It adopts special transmission belt with polyester core, high strength and high tensile performance.

The pulley adopts a squirrel cage structure with a slight protrusion in the middle, and each spoke is processed and chamfered. It not only improves the friction between the lifting tape and the pulley, avoids the slipping phenomenon of the old-fashioned light pulley and the belt pulley's slippage, but also reduces the pre-tightening force of the lifting belt and prolongs the service life; at the same time, it avoids the embedding of scattered bullets. Between the pulley and the belt, it affects the transmission.

There is a 10% margin for the increase. Because the hoist relies on centrifugal gravity to drop materials, part of the material will always fall back into the hoist every time it is dropped, so it is necessary to increase the lifting capacity appropriately.

- Pellet slag separator:

This machine adopts the most advanced full-curtain curtain air-selected pill slag separator in the world, and its separation efficiency is ≥99.5%. This separator is the latest separator of our company. The separator is one of the key components of the equipment, and the design size of the sorting area directly affects the separation effect of the separator. If the separation effect is not good, it will accelerate the wear of the blaster blades.

- Roller conveyor system

This machine uses a flat roller table; the running speed is stepless variable frequency speed regulation according to the corrosion degree of the steel, and the load-bearing capacity is 1000Kg per meter. The profile walks into the cleaning room to receive shot blasting, and the roller table has a V-shaped groove to prevent the round steel from rolling and blocking each other.

- Dust removal system

The dust removal system includes settling chamber, fan, motor, pipeline, etc.

- Electrical system

The electrical control system is suitable for three-phase AC 50HZ voltage 380V distribution circuit.

This machine adopts manual button control operation method, the low-voltage electrical components are all famous brand products, and the roller table adopts frequency converter control. The electrical system of this machine has the following characteristics:

The shot blasting device, the shot controller and the shot circulation system are all equipped with electrical interlocking and self-locking mechanisms to ensure the reliable operation of the equipment and the safety of the operators. The operation of the shot blasting device in this system is monitored and controlled by an ammeter. On the one hand, the shot blasting device can be protected by the ammeter, and on the other hand, it can monitor the phenomenon of empty throwing and blockage of the shot blasting device, so as to adjust the working status of the equipment at any time.