## Slide 1: Biofuel spray modelling
Dr. Ruslana Kolodnytska
Ass. Professor of Mechanical Engineering Department
Zhytomyr State Technological University, Ukraine
ERASMUS + /Mobility, May 2017, Coventry , UK
Ruslana Kolodnytsksa ruslanakolod@gmail.com Zhytomyr State Technological University, Ukraine
UKRAINE
UK

## Slide 2: Biofuels (biodiesel, ethanol) production
Thousand tonnes oil equivalent
years
regions
grew by
0.9%
[BP, 2016]

## Slide 3: What are the spray parameters of hemp biodiesel?
The LP-model can evaluate the spray penetration of a new type of alternative fuel in just 15 minutes!
ERASMUS +/ Mobility, May 2017, Coventry , UK
Ruslana Kolodnytsksa ruslanakolod@gmail.com Zhytomyr State Technological University, Ukraine
“To be a hemp biodiesel or not to be ?”
That is the question.
Ukraine is the 4th place in the world for technical hemp production

## Slide 4: CONTENT
Part I. Fuel spray
1. Spray parameters
2. Fluid parameters
Part II. Spray penetration
3. Correlations for diesel and biodiesel fuels
4. LP-model for biodiesel
5. LP-model for renewable diesel and Biofuel to Liquid (BTL) fuel.
Part III. Droplet distribution
6. Maximum entropy method
ERASMUS + teaching, May 2017, Coventry , UK
Ruslana Kolodnytsksa ruslanakolod@gmail.com Zhytomyr State Technological University, Ukraine

## Slide 5: Diesel fuel jet and droplet breakup
[Lee & Park, 2002]
[Lee & Park, 2002]
[Kuleshov, 2006]
Part I. Fuel spray
Fuel jet
Droplet breakup

## Slide 6: Simple Spray models
Lishevsky
Model, Ukraine
Roisman model, Germany
Kuleshov model (Diesel RK)
Part I. Fuel spray

## Slide 7: Main Spray parameters
[Assanis, 2011]
Spray penetration (SP) [Saszin, 2014]:
practical importance ( e.g. optimization of SP in internal combustion engine)
is easily measurable, so can be used for validation of the models
the correct prediction of the SP can indirectly indicate the correctness of complex models of spray formation
Spray penetration
Cone Angle
Sauter Mean Diameter
(SMD)
1. Spray parameters
Part I. Fuel spray

## Slide 8
SMD of Different Biodiesel (methyl esters of vegetable oils)
[ Kolodnytska R., 2006]
Part I. Fuel spray
1. Spray parameters

## Slide 9: Dimensionless fluid parameters
Parameter | Definition | Qualitative ratio | Importance
Reynolds Number | = |  | Always
Weber number | = |  | Free-surface flow
Drag coefficient | = |  | Aerodynamics, hydrodynamics
Parameter | Definition | Qualitative ratio | Importance
Reynolds Number |  |  | Always
Weber number |  |  | Free-surface flow
Drag coefficient |  |  | Aerodynamics, hydrodynamics
Part I. Fuel spray
2. Fluid parameters
Length parameter | = |  | New type of diesel fuels
Length parameter |  |  | New type of diesel fuels
Parameter | Definition | Qualitative ratio | Importance
New length parameter

## Slide 10: Biodiesel ligament breakup. Length parameter (LP)
Viscosity
Density
Surface tension
LP
[mm]
Primary atomization within first 2.1 mm from the nozzle for diesel (left) and biodiesel (right). Injection pressure is 40 MPa; gas pressure is 0.1 MPa [Crua et al., 2015]
Length and time parameters
for liquid jet breakup
Length parameter
for biodiesel spray SMD
[Kolodnytska, 2006]
Length parameter
for hemp biodiesel spray SMD
[Kolodnytska, 2010]
Part I. Fuel spray
[Eggers, 1997]

## Slide 11: Part II. Spray penetration

## Slide 12: Spray Penetration Modelling
Stip
S
Roizman model (2007)
Lishevsky model
Sazhin model (2005)
[Grabar IG, Kolodnytska RV, 2011]
Spray penetration: Stip
Part II.
Spray Penetration

## Slide 13: Spray Penetration Modelling, СOFM – model
[Kolodnytska RV. et al, International Congress of Propulsion Engineering, 2008]
Part II.
Spray Penetration

## Slide 14: Spray penetration correlations. Diesel fuels
Hiroyasu and Arai’s equations [Heywood, 1988]
University of Birmingham, UK [Wang Z. et al. , 2016]
Back Pressure | K1 | g | f
under 60 MPa | 0.14785/ 0.1520* | 0.02695/ 0.016* | -0.1047/ -0.034*
120 MPa | 0.7077 | 1.0917 | 0.6294
60 MPa | 0.7620 | 1.0713 | 0.7123
* Low temperature
Part II. Spray
penetration

## Slide 15: Physical properties of fuels
Case 1.
Physical properties [Kolodnytska, 2010] of biodiesel and diesel fuels, 80°C
 | HME * | SME | RME | Diesel
Density | 845 | 841 | 841 | 788
Kinematic viscosity | 1.96×10-6 | 2.01×10-6 | 2.58×10-6 | 1.09×10-6
Surface tension | 27.41×10-3 | 27.15×10-3 | 27.82×10-3 | 24.14×10-3
Case 2.
Physical properties [Desantes et al, 2009] of biodiesel and diesel fuels
 | Diesel | BDP | BDC
Density (15°C) | 830 | 874.4 | 885.1
Kinematic viscosity (30°C) | 3.36×10-6 | 5.53×10-6 | 4.45×10-6
Surface tension (25°C) | 25.5×10-3 | 26.2×10-3 | 25.7×10-3
Case 3.
New alternative to diesel fuels
 | Renewable diesel (HWO) | Biomass to Liquid (BTL)
HME –hemp oil biodiesel
SME – soy biodiesel
RME rapeseed oil biodiesel
BDP – biodiesel from palm oil
BDC – biodiesel from cooked oil
Part II. Spray penetration

## Slide 16: Biodiesel spray penetration
.
“spray momentum remains constant along the spray travel”
“the spray momentum flax was really similar for all fuels” (B5, B30, RME)
[Deasantes et al., 2009]
It has been found that injected mass of the fuel is influenced
by viscosity (when injection time is short)
by density ( when injection time is longer)
The injected mass was
lower with biodiesel for low injection time
higher when the time became longer
[Desantes et al., 2009] Universitat Politecnica de Valencia
is momentum flux
Part II. Spray penetration

## Slide 17: 3. LP-model for biodiesel
Part II. Spray penetration

## Slide 18: LP-model for spray penetration of biodiesel fuels
Spray Penetration is proportional to LP 0.1
LP [m] | 1.18×10-7 | 1.25×10-7 | 2.01×10-7 | 0.388×10-7
LP [micron ] | 11.8 | 12.5 | 20.1 | 3.88
Fuel | HME | SME | RME | Diesel
LP [m] | 3.67×10-7 | 10.21×10-7 | 6.81×10-7
LP [micron ] | 36.7 | 102.1 | 68.1
Fuel | Diesel | BDP | BDC
LP for biodiesels (Case 1, 80°C)
LP for biodiesels (Case 2)
Viscosity – Density -
Surface tension
Length parameter LP
Nozzle diameter - Injection pressure-
Gas density – LP- injection time [ms]
Part II. Spray penetration
Based on fuel properties:

## Slide 19: LP-model for biodiesel, 80 C (Case 1)
Spray penetration for diesel, RME and soy
biodiesel (SME). Injection pressure is 80 MPa.
Ambient pressure is 2 MPa.
The plots for hemp biodiesel (HME ) are very close
to SME and are not shown in the Figures .
Spray penetration for SME:
injection pressures 60 MPa, 80 MPA
comparing with experimental data.
Ambient pressure is 4 MPa.
ALP= 0.066 when the time tinj is in [ms]
Part II. Spray penetration

## Slide 20: LP- model for biodiesel (Case 2), 1
Diesel and biodiesel from cooked oil (BDC).
Gas density is 15 kg/m3; injection pressures are 100 MPa and 200 MPa
Diesel and biodiesels from cooked oil (BDC) and palm oil (BDP). Injection pressure is 200 MPa; gas density is 15 kg/m3
Chart: Time ASOI, ms
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2
diesel 100:15 | 0 | 24.2104 | 34.2387 | 41.9337 | 48.4209 | 54.1362 | 59.3032 | 64.0548 | 68.4775 | 72.6313 | 76.5602 | 80.297 | 83.8675
expDF 100:15 | 0 | 15 | 30 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 79 | 82 | 85
diesel 200:15 | 0 | 27.9651 | 39.5486 | 48.4369 | 55.9302 | 62.5318 | 68.5002 | 73.9887 | 79.0972 | 83.8953 | 88.4334 | 92.7497
expDF 200:15 | 17 | 33 | 48 | 58 | 63 | 67 | 73 | 78 | 84 | 85 | 89
BDC 200:15 | 0 | 29.5514 | 41.792 | 51.1845 | 59.1028 | 66.0789 | 72.3858 | 78.1856 | 83.5839 | 88.6542
expBDC 200:15 | 0 | 16 | 39 | 51 | 59 | 68 | 75 | 81 | 85 | 88
Chart: Time ASOI, ms
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001
diesel 200:15 | 0 | 27.9651 | 39.5486 | 48.4369 | 55.9302 | 62.5318 | 68.5002 | 73.9887 | 79.0972 | 83.8953 | 88.4334 | 92.7497
expDF 200:15 | 17 | 33 | 48 | 58 | 63 | 67 | 73 | 78 | 84 | 85 | 89
PDP 200:15 | 0 | 31.1988 | 44.1217 | 54.0378 | 62.3975 | 69.7625 | 76.421 | 82.5441 | 88.2434
expBDP 200:15 | 0 | 21 | 43 | 53 | 65 | 71 | 78 | 84 | 87
BDC 200:15 | 0 | 29.5514 | 41.792 | 51.1845 | 59.1028 | 66.0789 | 72.3858 | 78.1856 | 83.5839 | 88.6542
expBDC 200:15 | 0 | 16 | 39 | 51 | 59 | 68 | 75 | 81 | 85 | 88
Part II. Spray penetration

## Slide 21: LP- model for spray penetration of biodiesel fuels (Case 2), 2
Diesel and biodiesel from cooked oil (BDC).
Gas density is 15 kg/m3 ; injection pressure is 300 MPa
Diesel fuel ( diesel 300:30) and biodiesel from cooked oil (BDC 300:30). Injection pressure is 300 MPa; gas density is 30 kg/m3
Chart: Time ASOI, ms
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
BDP 300:15 | 0 | 33.4277 | 47.2739 | 57.8985 | 66.8554 | 74.7466 | 81.8808 | 88.4413 | 94.5478
expBDP 300:15 | 0 | 29 | 50 | 63 | 72 | 80 | 85 | 86 | 90
BDC 300:15 | 0 | 34.1956 | 48.3599 | 59.2286 | 68.3913 | 76.4638 | 83.7619 | 90.4731
expBDC 300:15 | 0 | 30 | 51 | 62 | 71 | 78 | 84 | 87
diesel 300:15 | 0 | 29.963 | 42.3741 | 51.8974 | 59.926 | 66.9993 | 73.394 | 79.2746 | 84.7481 | 89.889 | 94.7513
expDF300:15 | 16 | 36 | 50 | 59 | 69 | 74 | 79 | 85 | 88 | 90
Chart: Time ASOI, ms
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2
BDC 300:30 | 0 | 24.0528 | 34.0158 | 41.6607 | 48.1056 | 53.7837 | 58.9171 | 63.6377 | 68.0316 | 72.1584 | 76.0617 | 79.7741 | 83.3214
expBDC 300:30 | 0 | 12 | 27 | 40 | 48 | 55 | 60 | 64 | 69 | 72 | 75 | 80 | 85
diesel 300:30 | 0 | 22.7617 | 32.1899 | 39.4244 | 45.5233 | 50.8966 | 55.7545 | 60.2217 | 64.3797 | 68.285 | 71.9787 | 75.4919 | 78.8487
expDF 300:30 | 19 | 24 | 38 | 42 | 49 | 54 | 62 | 70 | 74 | 78 | 79
Part II. Spray penetration

## Slide 22: LP- model for spray penetration. The values of the coefficients ALP (Case 2)
The plots of BDP spray tip penetration Stip versus time of injection predicted by LP –model for biodiesel from palm oil (BDP 300:30). Experimental data of Stip for BDP (exp BDP 300:30) taken from [Figure 4, Wang, X., et al , 2010]. Injection pressure is 300 MPa; gas density is 30 kg/m3(300:30)
The values of the coefficients ALP for LP- model
Injection pressure/Gas density | Diesel | BDP | BDC
100 MPa/15.5 kg m-3 | 0.3 | 0.3 | 0.3
200 MPa/15.5 kg m-3 | 0.27 | 0.27 | 0.27
300 MPa/15.5 kg m-3 | 0.25 | 0.25 | 0.27
300 MPa/30 kg m-3 | 0.23 | 0.21 | 0.23
Chart: Time ASOI, ms
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2
BDP 300:30 | 0 | 23.1855 | 32.7893 | 40.1585 | 46.371 | 51.8444 | 56.7927 | 61.3431 | 65.5785 | 69.5565 | 73.319 | 76.8976 | 80.317
expBDP 300:30 | 0 | 19 | 32 | 40 | 48 | 53 | 55 | 62 | 66 | 70 | 73 | 77 | 80
LP 0.1 | 0.23 | 0.25 | 0.24
Fuel | Diesel | BDP | BDC
The values of the LP 0.1
Part II. Spray penetration

## Slide 23: LP- model for different alternative fuels. (Case 3)
Comparison of physical properties [Millo et al., 2015] and LP of biodiesel blends, HVO blend and diesel fuels
Fuel/ Properties | Diesel | RME 30 | HVO 30
Density (15°C) | 837.5 | 853 | 812.2
Kinematic viscosity (40°C) | 2.681×10-6 | 3.183×10-6 | 2.545×10-6
Surface tension (20°C) | 30.4×10-3 | 31.3×10-3 | 28.0×10-3
LP [m] | 1.98×10-7 | 2.76×10-7 | 1.88×10-7
LP 0.1 | 0.214 | 0.221 | 0.213
Comparison of physical properties [Dragomirov et. al, 2013] and LP of biodiesel and GTL
Fuel/ Properties | RME | GTL
Density (15°C) | 883 | 779.4
Kinematic viscosity (40°C) | 4.5×10-6 | 2.74×10-6
Surface tension (25°C) | 31.0×10-3 | 26.04×10-3
LP [m] | 5.77×10-7 | 2.25×10-7
LP 0.1 | 0.24 | 0.22
ERASMUS + teaching, May 2017, Coventry , UK
Ruslana Kolodnytsksa ruslanakolod@gmail.com Zhytomyr State Technological University, Ukraine
Part II. Spray penetration

## Slide 24: Evaluation of spray penetration for different alternative fuels using LP
Physical properties [Desantes et. al, 2009 ] and LP of biodiesel (RME) and RME blends
(CASE 3)
 | B5 | B30 | RME
Density (15°C) | 831 | 851 | 879
Kinematic viscosity (40°C) | 2.38 ×10-6 | 3.12×10-6 | 4.47×10-6
Surface tension (20°C) | 23.0×10-3 | 25.00×10-3 | 28×10-3
LP [m] | 2.05×10-7 | 3.31×10-7 | 6.27×10-7
LP 0.1 | 0.21 | 0.22 | 0.24
Physical properties [Crua et. al, 2015 ] and LP of diesel, biodiesel (RME) and kerosene.
(CASE 3)
 | RME | Diesel | Kerosene
Density | 883 | 837 | 803
Kinematic viscosity | 4.4×10-6 | 3.3×10-6 | 1.2×10-6
Surface tension | 33.2×10-3 | 29.8×10-3 | 27.7×10-3
LP [m] | 5.15×10-7 | 3.06×10-7 | 0.417×10-7
LP 0.1 | 0.24 | 0.22 | 0.18
Fuel | B5 | B30 | RME
LP 0.1 | 0.21 | 0.22 | 0.24
RME | Diesel | Kerosene
0.24 | 0.22 | 0.18
Fuel | Diesel | RME 30 | HVO 30
LP 0.1 | 0.214 | 0.221 | 0.213
RME | GTL
0.24 | 0.22
LP 0.1 (CASE 3 )
Part II. Spray penetration

## Slide 25: Part III. Droplet distribution

## Slide 26: Droplet diameter distribution diesel (line -) biodiesel (-----)
10 mm from nozzle 15 mm from nozzle
Part III. Droplet Distribution
[Experiments: C. Crua, Brighton and BP, 2007]

## Slide 27: Maximum Entropy Method, 1
Weber number
Mass mean droplet diameter
Sources for mass, momentum , energy
D30
Part III. Droplet Distribution

## Slide 28: Maximum Entropy Method,2
Classic dependence between the system entropy and the probability of microstates
The probability density function:
The maximal value of the entropy was
found by the Lagrangian multiplier method
Part III. Droplet Distribution

## Slide 29: Application of MA method to biodiesel spray
Probability density function at distance from the nozzle of 15 mm.
Injection pressure 100 MPa, ambient atmospheric pressure,
Delphi nozzle ( 0.135 microns)
Diesel
Biodiesel
Weber number
We = 2500
Part III. Droplet Distribution

## Slide 30: Conclusions
Simple model (LP-model) for biodiesel spray penetration under conditions relevant to internal combustion engines was proposed.
A parameter referred to as “length parameter” (LP) is introduced to define the fuel properties.
Spray penetrations for Biodiesels from Hemp oil, Rapeseed oil, Soybean oil, Palm oil and Cooked oil comparing with those of diesel fuel were calculated under different injection conditions and ambient pressures.
The model gives a good agreement with experimental data that available for biodiesel and diesel fuels.
Length parameters of new types of alternative diesel fuels: Hydrogenated Vegetable Oil (HVO) and Biomass to Liquid (BTL) were evaluated.
ERASMUS + teaching, May 2017, Coventry , UK
Ruslana Kolodnytsksa ruslanakolod@gmail.com Zhytomyr State Technological University, Ukraine

## Slide 31: Literature
Sazhin S.S., Al Qubeissi M., Kolodnytska R., Elwardany A.E., Nasiri R., Heikal M.R. Modelling of biodisel fuel droplet heating and evaporation. Fuel 115 (2014), 559-572.
Sazhin S. Droplets and Sprays. Springer. 2014
Grabar IG, Kolodnytska RV, Semenov VG. Biofuels for diesel engine. 2011(In Ukrainian)
Kolodnytska R.V. Analytical study for atomization of hemp oil biodiesel. //Visnik SNU im. Volodimira Dalya.- 2010- №6 (148).- P.41-46 (In Ukrainian).
Kolodnytska R. LP-model for Biodiesel Spray Penetration. ILASS – Europe 2016, 27th Annual Conference on Liquid Atomization and Spray Systems, 4-7 September 2016, Brighton, UK.

## Slide 32
Hemp biodiesel
Or hemp BTL?
Thank you !
ERASMUS + teaching, May 2017, Coventry , UK
Ruslana Kolodnytsksa ruslanakolod@gmail.com Zhytomyr State Technological University, Ukraine
The next lecture is “Hemp car”

## Slide 33: What is the future alternative diesel fuels?
“Renewable diesel easily replaces petroleum diesel with no equipment modifications and no expensive infrastructure changes”
http://www.aiche.org/chenected/2016/02/renewable-diesel-big-winner-after-paris-climate-accord-and-vws-diesel-gate
ERASMUS + teaching, May 2017, Coventry , UK
Ruslana Kolodnytsksa ruslanakolod@gmail.com Zhytomyr State Technological University, Ukraine